Supplementary Table 1. Comparison of traditional and modified RA technique
	Traditional	Modified
Initial burr size	Plaque modification with small burrs (1.25 mm to 1.5 mm) as initial strategy is default position.	1)≧1.75 mm if IVUS/OCT can cross the lesion； / 2)≦1.5 mm if IVUS/OCT can not cross the lesion.
Ablation speed	Plaque modification usually achieved at low speeds (135,000 to 180,000 rpm) to reduce risk of complications.	Pass at "high" speed (160,000–220,000 rpm); / then polish at “low” speed (140,000–160,000 rpm).
RA flush	Rotablation cocktail with verapamil, nitrates and heparin in saline recommended	Double flush: RA-cocktail shower + intracoronary flush-cocktail from guiding catheter
Burr motion	Pecking motion	Cruising motion

Supplementary Table 2. Baseline lesion characteristics of the patients (n=1169)
Characteristics	No. patients (%) or median (IQR)
De novo lesion	970 (83.0)
ISR lesion	199 (17.0)
Target vessel
LMT	40 (3.4)
LAD	660 (56.5)
LCX	189 (16.2)
RCA	298 (25.5)
Extent of the disease
Single vessel disease	759 (64.9)
Double vessel disease	295 (25.2)
Triple vessel disease	115 (9.8)
Bifurcation lesion	640 (54.7)
Ostial lesion	494 (42.3)
CTO	59 (5.0)
Lesion type (AHA)
A	0 (0)
B1	2 (0.2)
B2	189(16.2)
C	978 (83.7)
Pre-QCA
Reference vessel diameter (mm)	2.72 (2.37–3.20)
Lesion length (mm)	30.67 (22.78–39.91)
Lesion angulation >45°	618 (52.9)

AHA, American Heart Association; CTO, chronic total occlusion; LAD, left anterior descending artery; LCX, left circumflex coronary; LMT, left main trunk; QCA, quantitative coronary angiography; RCA, right coronary artery.
Supplementary Table 3. PCI procedure and QCA data (n=1169)
Characteristics	No. Patients (%) or median (IQR)
PCI strategy
RA+DES	798 (68.3)
RA+DCB	59 (5.0)
RA+POBA	312 (26.7)
Guiding catheter ≥7 (F)	596 (51.0)
Femoral approach	550 (47.0)
Fluoroscopy time (min)	25.15(18.73–34.08)
Contrast volume (ml)	188(157–227)
Maximum stent diameter (mm)	3 (2.50–3.50)
Maximum burr size (mm)	1.75 (1.50–1.75)
Maximum balloon diameter (mm)	3 (2.50–3.50)
Maximum balloon pressure (atm)	20 (14–24)
Maximum burr-to-artery ratio	0.63 (0.55–0.73)
Maximum balloon-to-artery ratio	1.11 (1–1.28)
Maximum stent-to-artery ratio	0.97 (0–1.10)
Minimum rotational speed	140000 (120000–160000)
Total stents length (mm)	38.00 (24 –38)
No. of burrs used (≥2)	402 (34.4)
No. of stents used	1 (0–1)
Immediate QCA
MLD before PCI (mm)	0.95 (0.70–1.21)
% DS before PCI	63 (56–72)
MLD after PCI (mm)	2.73 (2.31–3.19)
% DS after PCI	2.00 (-7.00–13.00)
Acute gain (mm)	1.75 (1.36–2.10)
Image device	1065 (91.1)
PCI complications	26 (2.2)
Perforation	20 (1.7)
Slow/no flow	5 (0.4)
Burr trap	1 (0.1)

BMS, bare metal stent; DCB, drug-coated balloon; DES, drug-eluting stent; MLD, minimal lumen diameter; POBA, plain old balloon angioplasty; QCA, quantitative coronary angiography; RA, rota­tional atherectomy; %DS, percent diameter ste­nosis.

Supplementary Table 4. Predictors of target lesion revascularization
Variables	Univariate					Multivariable
	cHR	95% CI	P-value			aHR	95% CI	P-value
Demographic characteristics
Age(1-year increase)	0.98	0.96-1.00		0.056
Life behavior
Current smoker	1.33	0.83–2.11		0.237
Medical situation
Hypertension	1.60	0.81-3.16		0.181
Diabetes	1.98	1.40–2.81		<0.001		1.70	1.18–2.47		0.005
Hyperlipidemia	1.11	0.73–1.67		0.627
Hemodialysis	3.68	2.45–5.52		<0.001		3.03	1.96–4.68		<0.001
LVEF	0.97	0.96–0.99		0.001		0.99	0.97–1.01		0.066
Lesion characteristics
Reference vessel diameter	1.36	1.05-1.76		0.021
Lesion length	0.99	0.99–1.01		0.907
Treatment
PCI strategy
RA+DES (Ref)	1.00					1.00
RA+DCB	4.81	2.74–8.45		<0.001		4.53	2.54–8.06		<0.001
RA+POBA	3.17	2.20–4.58		<0.001		2.76	1.87–4.08		<0.001
Maximum burr/artery ratio	2.57	0.95–6.99		0. 064
MLD after PCI	0.84	0.62–1.12		0. 237
Statin used	1.33	0.94–1.90		0.112

aHR, adjusted hazard ratios; CI, confidence interval; cHR, crude hazard ratios; DCB, drug-coated balloon; DES, drug-eluting stent; LVEF, left ventricular ejection fraction; MLD, minimal lumen diameter; POBA, plain old balloon angioplasty; RA, rota­tional atherectomy.

Supplementary Figure 1. Cumulative incidence curves for (A) major adverse cardiac events (MACE), (B) all-cause death, (C) target lesion revascularization (TLR) and (D) cardiac death.

Supplementary Figure 2. Comparison of MACE among different PCI strategies. DCB, drug-coated balloon; DES, drug-eluting stent; MACE, major adverse cardiac events; POBA, plain old balloon angioplasty; RA, rota­tional atherectomy.